­FANCLUB MARK II NETWORKING SPECIFICATION
Revised Jan.10th 2018

GENERAL STANDARD
–To be followed by both Master and Slaves.

HANDSHAKE PROTOCOL

1. Master and Slave initialize their Ethernet interfaces separately.
2. Master sends UDP "general broadcast":
XXXXX fcmkii
Where XXXXX is Master’s listener socket port number. e.g “52147 fcmkii”.
3. Slave finds broadcast and sends reply to given listener socket:
XXXXX YYYYY ZZ:ZZ:ZZ:ZZ:ZZ:ZZ
Where XXXXX is Slave’s MISO socket port number, YYYYY is Slave’s MOSI socket port number, and ZZ:ZZ:ZZ:ZZ:ZZ:ZZ is Slave’s MAC address.
4. Master receives reply and either initiates connection or lists Slave as AVAILABLE.
(*. The following steps happen within connect() method once Master initiates a connection)
5. Master reaches out to Slave using port numbers given in step 4:
XXXXX YYYYY ZZ:ZZ:ZZ:ZZ:ZZ:ZZ
Where XXXXX is Master’s MISO socket port number, YYYYY is Master’s MOSI socket port number, and ZZ:ZZ:ZZ:ZZ:ZZ:ZZ is Slave’s MAC address.
NOTE: At this step, more than one attempt may be made by Master before assuming failure.
6. Slave receives message in MOSI socket and sends "ACK" to MISO.
7. Master receives "ACK" from Slave, sends one last "ACK" and marks Slave as CONNECTED.

NOTE: Errors in 5. and 6. will result in Slave being marked as DISCONNECTED and its network attributes (ip, mosi and miso) set to None and "RIP" sent to Slave. In step 7, Slave may request verification by sending "VER" to MISO. Errors in previous steps will result in a new attempt in the next broadcast. Note that once a Slave is chosen by the user, Master will automatically go for reconnection whenever possible. Lastly, "errors" in this context refer solely to UDP messages being lost.

COMMUNICATIONS PROTOCOL

Once a connection is established, the following exchange is maintained until disconnection.

1. Master checks for outgoing messages. If there is no outgoing message, it sends a standard verification message:

XXXXXXXXXXX (Some specified message)
or:
V MOSI (Standard verification message)

Here NN is the message number

2. Either Slave receives message or [...]
MASTER SPECIFICATION
–Details specific to Master

POSSIBLE SLAVE STATUSES:

STATUS	MEANING	CONNECTED?	IP	MISO/MOSI	Queues	Thread
KNOWN	Slave has been previously chosen for connection and should be connected to automatically.	NO	None	None	None	None
AVAILABLE	Available Slave has been detected in the network and a connection can be made if indicated.	NO	IP (str)	MISO/MOSI port numbers	None	None
CONNECTED	Slave is currently connected to Master.	YES	IP (str)	MISO/MOSI sockets	MISO/MOSI queues	Slave thread
BUSY	Slave is connected but is currently processing a command and cannot accept new commands.	YES	IP (str)	MISO/MOSI sockets	MISO/MOSI queues	Slave thread
DISCONNECTED	Slave was previously connected and said connection was lost or terminated.	NO	None	None	None	None

SLAVE SPECIFICATION
–Details specific to Slave.

On the Slave-side, communication with Master is handled entirely by the Communicator module, which operates in two threads – the “broadcast thread” and the